## Slide 1: 電路模擬器 MiniPSPICE
B09901034 戴瑋佑 B09901170 黃元顥 B09901175 楊博宇

## Slide 2: Table of contents
Introduction
DC Analysis (with multiple voltage sources)
AC Analysis (with one voltage source)

## Slide 3: Introduction
B09901170 黃元顥

## Slide 4: Procedure
Target Circuit
Description
Simulation

## Slide 5: Circuit Description
Assign nodes
AC/DC (specify frequency for AC)
Components
  Voltage Source: V mag (phase) node+ node-
  Resistor: R value node1 node2
  Inductor: L value node1 node2
  Capacitor: C value node1 node2
Specify node display order: & node1 node2 …
Comments: # (whole line), // (behind)
Units are in Hz, Ohm, H, F
A
D
B
C

## Slide 6: Result
Generate circuit diagram
Calculate voltage of each node
Calculate terminal voltage of each component

## Slide 7: Main Structure

## Slide 8: DC Analysis
B09901175 楊博宇

## Slide 9: Nodal Analysis
Take one node as the ground node.
Select node voltages (vs. ground) as the variables.
If node voltages are known, all the other branch variables can be calculated.

## Slide 10: Constraints
A node is allowed to connect at most one voltage source.
The input file should represent a closed circuit.
Any voltage source is not allowed to be short-circuited.
The second node of the first voltage source that you input will be connected to the ground, which is referred to as the ground node.
In a DC circuit, if we just concern the steady state, Inductor (L) short-circuit, and Capacitor (C) open-circuit.

## Slide 11: Procedure
Suppose that there are nodes initially.
Merge nodes connecting to inductors, and there are nodes left.
Distribute these nodes into two lists, ‘n_left’ and ‘n_removed’, containing and nodes respectively.
Construct the conductance matrix () by nodal analysis.

## Slide 12: Procedure
Complete as a square matrix by the supernode technique. (If the remaining equations are linear dependent, replace one of which by letting the node connecting to the ground be 0.)
Compute the list of every node voltage by .
Separate the nodes connecting to the inductors. ()
Subtracting each element by the voltage of the ground node, we are able to obtain the voltage of each node in the circuit.

## Slide 13: Code Explanation(1/5): Setting variables

## Slide 14
Code Explanation(2/5): Merging nodes connecting to L

## Slide 15
Code Explanation(3/5): Constructing the matrix G

## Slide 16
Code Explanation(4/5): Solving the node voltage

## Slide 17
Code Explanation(5/5): Obtaining the answer

## Slide 18: Demonstration
DC
V 7 A F
V 1 B C
R 5 A B
R 2 C D
L 2 C D
R 2 D E
R 3 E F
& A B C D E F
Input
Output

## Slide 19: AC Analysis
B09901134 戴瑋佑

## Slide 20: Node analysis
Take this circuit for example first. According to node analysis, we can list the formula
A
D
B
C

## Slide 21: Node analysis
Assume the ground() at D →
Source :
KCL_B :
KCL_C :
A
D
B
C

## Slide 22: Node analysis
A
D
B
C

## Slide 23
程式說明

## Slide 24
程式說明

## Slide 25
程式說明

## Slide 26
程式說明

## Slide 27
程式說明

## Slide 28
輸出結果
A
D
B
C

## Slide 29: Thank you for listening!